## Slide 1
Smart Facility Digital Twin
Predictive maintenance for building HVAC
6 rooms · 2 floors · 11 interacting twins · 1 machine-learning model
Notes: This is a working system, not a concept. Everything shown runs.

## Slide 2
THE PROBLEM
We find HVAC failures when someone complains
• In a wet lab, that means temperature-sensitive samples are already at risk.
• Maintenance runs on a calendar: we service units that don't need it…
• …and miss units that do.
• No visibility into equipment condition between visits.
The question isn't whether to maintain.
It's whether we maintain on a calendar or on evidence.
Notes: The question isn't whether to maintain. It's whether we maintain on a calendar or on evidence.

## Slide 3
WHAT WE BUILT
A digital twin for every room
• Physics, control and equipment health simulated per room, live over MQTT.
• Floor and building twins coordinate a 15 kW electrical budget.
• An occupancy twin moves people between rooms — conserving headcount.
• Dashboard, 3D building view, and machine-learning risk scoring.
Notes: Each room runs its own control loop. Supervisors advise; they never take over. If the coordination layer dies, every room keeps cooling.

## Slide 4
ARCHITECTURE
Rooms decide. Supervisors advise.
 | Centralised | Federated (chosen)
A crash stops… | every room cooling | coordination only
Occupancy data | leaves every room | stays room-local
Tuning | one loop for all rooms | per-room thermal mass
A supervisor bug | actuates every room | bounded advice, ≤1.5 °C
The 1.5 °C limit is enforced by the room, not by the supervisor sending the advice.
Notes: One crash in a centralised design stops every room. And occupancy data would have to leave the room it came from — this is a privacy choice as much as a resilience one.

## Slide 5
THE INTELLIGENCE
Four hours of warning before a failure
PR-AUC 0.92
Recall 0.95
Precision 0.66
Accuracy would be 98 % if we always predicted
"no failure". That is why we don't quote it.
Notes: Accuracy would be 98% if we simply predicted 'no failure' every time — that's why we don't quote accuracy. The model is six times better than the obvious rule.

## Slide 6
LIMITATIONS
What the model cannot do
Blind to heat-dissipation
failure on its own.
About two such events existed in the
training data. No model learns from two.
A physics threshold covers it — we ship
both, and report them separately.
Notes: This is the slide I'd want to see if I were buying. ML is not uniformly better than rules — it beats thresholds on cumulative wear and loses to a thermostat on a fault with a direct physical precursor. We ship both.

## Slide 7
FAIRNESS AUDIT
Weakest where it matters most
Wet Lab A:
100 % of failures missed
Not because the model knows which room it
is looking at — room identity is excluded.
That room is serviced so well its only
failures are the mode the model can't see.
Keep calendar servicing there.
Notes: The room the model covers worst is the room where failure costs most. We found it, published it, and mitigate it with the thermal guard — but keep calendar servicing on that unit. We are not asking you to trust it there.

## Slide 8
BUSINESS CASE
Where the value actually is
≈ €5,800 / year
Anyone pitching predictive maintenance
on fan energy alone is selling you
something. The value is in outages
you don't have.
Notes: The energy saving is real but small — €155. The value is in outages you don't have.

## Slide 9
THE UNCOMFORTABLE NUMBER
At six units, it does not pay for itself
One-off investment | €17,000
Recurring | €2,900 / year
Net benefit | €2,900 / year
Payback | 5.9 years
5-year NPV @ 8 % | −€5,420
Integration cost is roughly fixed.
Benefits scale with unit count.
This is a question of scale —
not of whether the technology works.
Notes: On this building alone, it does not pay for itself. Integration cost is roughly fixed; benefits scale with unit count.

## Slide 10
RECOMMENDATION
Where it does pay
Pilot to prove the model
on real telemetry.
Then scale to campus.
Not a building-by-building rollout.
Notes: The recommendation is a pilot to prove the model on real telemetry, then campus scale. Not a building-by-building rollout.

## Slide 11
SECURITY
The pilot is not secure — and that is costed
• Today: anonymous broker, no encryption. Fine on one machine.
• Unacceptable in a building that dispatches technicians.
Hardening | Why
mTLS + per-topic ACLs | a room twin can only speak for itself
Signed commands | no replay, no spoofed shutdown
Audit log | every action attributable to a person
Network segmentation | not routable from the office LAN
€4,000 — a line item, not a backlog ticket.
Notes: A system that dispatches technicians to physical equipment needs every command attributable to a person. That's in the budget, not the backlog.

## Slide 12
ETHICS AND OVERSIGHT
The model opens tickets. It never switches anything off.
• Every advisory carries requires_human_approval.
• Supervisory autonomy is bounded at 1.5 °C — enforced by the room.
• Occupancy is counted, never identified, and stays in the room that produced it.
• Known limitations are shown in the dashboard, not just in the appendix.
There is no path from a model score to a physical action
that does not pass through a person.
Notes: There is no path from a model score to a physical action that doesn't pass through a person.

## Slide 13
THE ASK
Phase 1: instrumented pilot
Scope | 3 units, one floor, observe-only
Duration | 3–6 months
Exit criterion | model recalibrated on REAL telemetry; fairness audit repeated
Named risk | real failures are rare — may see zero events; run in shadow mode
Approve Phase 1, and the €4,000 security hardening up front.
Everything today is built on simulated data. The failure physics is calibrated against a published
industrial dataset, but no number in this business case is trustworthy until it has been seen on
this building. Phase 1 exists to find that out cheaply.
Notes: Everything today is built on simulated data. Phase 1 exists to find out cheaply whether it holds on this building.