## Slide 1
Smart Facility Digital Twin
Project 2 — Intelligent Ecosystem & Strategic Optimization
2 floors · 6 rooms · 11 interacting twins · 5 predicted failure modes
Extends the Project 1 single-room twin into a coordinated, self-monitoring facility.
Notes: Project 2 report. Everything shown runs; nothing is mocked.

## Slide 2
BRIEF
Objective & scope
• Extend one room twin into an intelligent, autonomous ecosystem.
• Integrate a predictive model for equipment failure.
• Coordinate multiple interacting twins across a smart facility.
• Address governance, ethics, ROI and a deployment roadmap.
Key task | Delivered by
Predictive Intelligence | 5-class fault model + physics guard, live per room
Ecosystem Integration | 11 twins, federated coordination, MQTT data flows
Governance & Ethics | Threat model, fairness audit, bounded autonomy
Strategic Roadmap | Measured ROI, 4-phase pilot-to-campus plan
Notes: Four key tasks from the brief, and where each is answered.

## Slide 3
WHAT CHANGED
From one room to a facility
 | Project 1 | Project 2
Scope | 1 room | 2 floors, 6 rooms, 11 twins
Coordination | None | Federated — rooms decide, supervisors advise
Occupancy | Per-room random walk | Headcount-conserving people flow
Equipment | Never degrades | 5 failure modes, AI4I-calibrated
Intelligence | PID control | PID + fault-type model + thermal guard
Remediation | AC on/off | 5 remedies, manual or model-dispatched
The Project-1 room survives as f1/lab-a with its calibrated constants intact — a test locks them as the regression guard.
Notes: Project 1's room is still here, unchanged, as the regression guard for the whole refactor.

## Slide 4
ECOSYSTEM INTEGRATION
Eleven twins, each with one job
Twin | Count | Owns | Loop
Room twin | 6 | Physics, PID, equipment health | 1 s
Floor twin | 2 | Aggregate; recommend setpoint nudges | 10 s
Building twin | 1 | kW allocation; maintenance work orders | 30 s
Occupancy twin | 1 | People flow between rooms | 1 s
Risk scorer | 1 | Fault probability per room | 30 s
Occupancy → energy → equipment wear → maintenance is a single causal chain.
A class leaving one room raises load in another, which accrues wear, which the model sees hours later.
Notes: The brief asks for an energy twin interacting with an occupancy twin. That path is real: headcount is conserved, so people genuinely move between rooms and the thermal load follows them.

## Slide 5
DELIVERABLE — COORDINATION STRATEGY
Centralised vs federated
 | Centralised | Federated (chosen)
A crash stops… | every room cooling | coordination only
Local disturbance | waits for the global loop | handled in the room's own 1 s loop
Occupancy data | leaves every room | stays room-local; aggregates only
Tuning | one loop for a 20 m² and a 70 m² room | per-room thermal mass
A supervisor bug | actuates every room | bounded advice, ≤ 1.5 °C
The 1.5 °C limit is enforced by the room, not by the supervisor sending the advice — so a spoofed or buggy advisory cannot make a room unsafe. Eight named tests back these claims.
Notes: Federated with hierarchical supervision. Authority flows downward as advice and stops at a bound the recipient owns.

## Slide 6
PREDICTIVE INTELLIGENCE
Five failure modes, one per unit character
Unit | Fails by
Wet lab A | Airflow
Dry lab B | Bearing
Server room | Overstrain
Teaching lab C | Heat dissipation
Meeting room | Power
Thresholds inherit from UCI AI4I 2020, whose published rules we verified reproduce exactly (115/115 rows).
Notes: Real buildings do not contain six identical units. Each has its own wear character, which is what makes fault classification a real problem rather than one class with noise.

## Slide 7
DELIVERABLE — PREDICTIVE MODEL OUTPUT
Model results
PR-AUC 0.953
Recall 0.974
Precision 0.734
Decision threshold 0.0153, chosen from a
cost curve — not left at 0.5.
Accuracy would be 97 % if we always
predicted "no failure". That is why
it is not the headline.
Notes: Trained and evaluated with a temporal split and a held-out room. A random shuffle would inflate this to a meaningless 0.99.

## Slide 8
PREDICTIVE INTELLIGENCE
Every mode detected — after a correction
Heat dissipation:
0.00 → 0.93 recall
The first model was blind to that mode.
It had seen about two examples of it.
The cause was starvation, not tuning:
six identical units meant one mode
was 90 % of the data. Fixing the DATA
fixed the model.
A physics threshold still backs it up.
Notes: A model that cannot see a failure mode is usually being starved of it, not badly tuned. Worth stating because it generalises.

## Slide 9
GOVERNANCE & ETHICS
Fairness audit
Recall 0.89–1.00
in every room
Room identity is excluded from the
features by construction, so the model
cannot learn a per-room prior.
Teaching Lab C stays weakest:
precision 0.45, and it misses about
one failure in nine.
The audit is repeated after every retrain.
Notes: An earlier version had a 100 % false-negative rate on the wet lab — the room where an outage costs most. We publish both states.

## Slide 10
ECOSYSTEM INTEGRATION
Closing the loop: one remedy per mode
Fault | Remedy | Reduces cooling?
Airflow | Replace filter | No
Bearing | Service motor | No
Overstrain | Service motor + occupant notice | No
Power | Electrical service | No
Heat dissipation | Thermal derate — cap fan duty | Yes, bounded
The derate is capped at 50 % duty, never zero, and releases itself once the winding cools —
what a thermal overload relay does. Easing a motor off is not the same act as switching cooling off.
Notes: The system used to predict five faults and fix two. Three predictions had no action anyone could take.

## Slide 11
GOVERNANCE & ETHICS
Security — the honest posture
• The pilot broker is anonymous and unencrypted. Fine on one machine.
• Unacceptable in a building that dispatches technicians to equipment.
Hardening | Why
mTLS + per-topic ACLs | a room twin can only speak for itself
Signed commands | no replay, no spoofed shutdown
Append-only audit log | every action attributable to a person
Network segmentation | not routable from the office LAN
Costed at €4,000 — a line item, not a backlog ticket.
Notes: Stating the pilot is insecure is more useful than claiming otherwise. The threat model and checklist are in governance.md.

## Slide 12
GOVERNANCE & ETHICS
Bounded autonomy, in one operator control
Level | Thermostat runs the AC | Model dispatches maintenance
Manual | No | No
Auto climate (default) | Yes | No — approval required
Full auto | Yes | Yes — preventive actions only
• Full auto is never the default — autonomy is opted into.
• Preventive actions only; at most one automatic service per unit per 24 h.
• Every dispatch is still published as an advisory, so the audit trail is identical.
• Shutting a unit down is forbidden at every level.
Notes: There is no path from a model score to a physical action that does not pass through a person, or through these bounds.

## Slide 13
STRATEGIC ROADMAP
Where the value is — and is not
≈ €5,929 / year
Fan energy is measured: 620 kWh, €155.
Small. Anyone pitching predictive
maintenance on fan energy alone is
selling you something.
The value is in outages you don't have.
Notes: Every figure is labelled measured or assumed. The cooling-capacity loss is probably larger and we do not claim it, because we did not measure it.

## Slide 14
STRATEGIC ROADMAP
At six units it does not pay for itself
One-off | €17,000
Recurring | €2,900 / yr
Payback | 5.7 years
5-yr NPV @ 8 % | −€5,021
Integration cost is roughly fixed;
benefits scale with unit count.
Recommendation: pilot to prove the
model on real telemetry, then scale
to campus — not building by building.
Notes: Reporting a negative NPV is the point. The conclusion is robust across the sensitivity table.

## Slide 15
STRATEGIC ROADMAP
Pilot to campus
Phase | Scope | Exit criterion | Named risk
0 — Pilot (complete) | 6 simulated twins | Suite green; loop verified end to end | All results rest on simulated data
1 — Instrumented 3–6 months | 3 real units, observe-only | Model recalibrated on REAL telemetry | Real failures are rare; may see zero
2 — Full building 6–12 months | All units, live work orders | Measured drop in unplanned outages | Alert fatigue at 0.73 precision
3 — Campus 12–24 months | ≥ 24 units | Positive measured NPV | Models transfer poorly (PR-AUC 0.20)
Phase 4 — bounded autonomy — only after Phase 3, and never automatic shutdown.
Notes: Each phase has an entry criterion, an exit criterion and a named risk with its mitigation.

## Slide 16
REPRODUCIBILITY
Working prototype — how to run
docker compose up -d
dashboard http://localhost:8501
3D view http://localhost:8000/room3d/building3d.html
docker compose run --rm sim pytest -v
docker compose run --rm sim python simulator/dataset_generator.py
docker compose run --rm sim python ml/train.py
• Everything runs in Docker — no host Python needed.
• The dataset and both models regenerate from source, deterministically.
• Notebooks in ml/notebooks/ carry executed output.
Notes: One command brings up the broker, simulator, dashboard and 3D view. The full suite runs in the same image.

## Slide 17
CONCLUSION
Deliverables
Required deliverable | Where
Predictive model output — notebooks / results | ml/notebooks/*.ipynb · ml/models/model_card.md
Integrated ecosystem diagram — coordination strategy | docs/ecosystem.md (data flow, sequence, centralised vs federated)
Executive pitch — ROI, security, ethical safety | report/pitch/Digital_Twin_Project2_Executive_Pitch.pptx
Predictive intelligence (key task) | 5-class model + thermal guard, live per room
Ecosystem integration (key task) | 11 twins, federated coordination, MQTT topic map
Governance & ethics (key task) | docs/governance.md
Strategic roadmap (key task) | docs/roi_roadmap.md
All results are reproducible from a clean clone. The models are trained on simulated telemetry — recalibration on real data is Phase 1.
Notes: Closing slide: every required deliverable and where to find it, with the standing caveat about simulated data.